# Raspberry Pi Lab: Demonstrating Interrupts and Buses
## Objectives
- Learn how to handle interrupts using GPIO on the Raspberry Pi.
- Understand buses by communicating with an I2C sensor.
- Develop a Python program to interact with hardware components.
## Materials Required
- Raspberry Pi with GPIO support
- Passive Infrared (PIR) Motion Sensor (for GPIO interrupt demo)
- Sonar Sensor (Data I/O) to measure distance.
- I2C Temperature Sensor (e.g., BMP280 or DS3231 RTC) for I2C communication
- Breadboard and jumper wires

## Part 1: Setting Up an Interrupt Using GPIO
### Step 1: Wiring the PIR Sensor
The PIR motion sensor has three pins:
- VCC → 5V (or 3.3V depending on model)
- GND → Ground
- OUT → Connect to GPIO 17 (Pin 11) on Raspberry Pi
### Step 2: Writing an Interrupt Handling Script
Create a Python script gpio_interrupt.py:
import RPi.GPIO as GPIO
import time

def motion_detected(channel):
    print("Motion detected!")

# Set up GPIO
GPIO.setmode(GPIO.BCM)
PIR_PIN = 17
GPIO.setup(PIR_PIN, GPIO.IN)

# Add event detection
GPIO.add_event_detect(PIR_PIN, GPIO.RISING, callback=motion_detected)

try:
    print("Monitoring for motion. Press Ctrl+C to exit.")
    while True:
        time.sleep(1)
except KeyboardInterrupt:
    print("Exiting...")
    GPIO.cleanup()
#### Explanation
- The script sets up GPIO pin 17 as an input.
- Uses GPIO.add_event_detect() to register an interrupt on a rising edge signal.
- The callback function motion_detected() runs when motion is detected.
- The program runs continuously, monitoring for motion.

## Part 2: Measuring Distance with a Sonar Sensor
### Step 1: Connect the HC-SR04 Ultrasonic Sensor
The HC-SR04 sonar sensor can measure distance by emitting ultrasonic waves and measuring the time it takes for them to return after bouncing off an object.
Connect the sensor to the Raspberry Pi as follows:
- VCC → 5V
- GND → Ground
- TRIG → GPIO 23 (Pin 16)
- ECHO → GPIO 24 (Pin 18)
### Step 2: Write a Distance Measurement Script
Create a Python script sonar_distance.py:
import RPi.GPIO as GPIO
import time

# Define GPIO pins for TRIG and ECHO
TRIG = 23
ECHO = 24

GPIO.setmode(GPIO.BCM)
GPIO.setup(TRIG, GPIO.OUT)
GPIO.setup(ECHO, GPIO.IN)

def measure_distance():
    # Send a 10 microsecond pulse to TRIG
    GPIO.output(TRIG, True)
    time.sleep(0.00001)
    GPIO.output(TRIG, False)

    # Wait for ECHO to go high and measure the time
    while GPIO.input(ECHO) == 0:
        start_time = time.time()

    while GPIO.input(ECHO) == 1:
        stop_time = time.time()

    # Calculate the distance based on time of flight
    time_elapsed = stop_time - start_time
    distance = (time_elapsed * 34300) / 2 # Convert to centimeters
    return distance

try:
    while True:
        dist = measure_distance()
        print(f"Distance: {dist:.2f} cm")
        time.sleep(1)
except KeyboardInterrupt:
    print("Exiting...")
    GPIO.cleanup()
### Explanation
- The script uses the TRIG pin to send a 10-microsecond pulse to start the measurement.
- The ECHO pin listens for the return signal and measures the time of flight.
- The distance is calculated based on the speed of sound (34

## Part 3: Communicating with an I2C Sensor
### Step 1: Enable I2C on Raspberry Pi
Run the following command to open the configuration tool:
sudo raspi-config
Navigate to Interfacing Options → I2C → Enable. Reboot the Raspberry Pi.
### Step 2: Install Required Libraries
For a BMP280 sensor, install the smbus library:
sudo apt-get install python3-smbus
### Step 3: Connect the I2C Sensor
Wire the BMP280 sensor:
- VCC → 3.3V
- GND → Ground
- SCL → GPIO 3 (I2C Clock, Pin 5)
- SDA → GPIO 2 (I2C Data, Pin 3)
### Step 4: Read Data from the Sensor
Create a Python script i2c_sensor.py:
import smbus
import time

i2c_bus = smbus.SMBus(1) # Use I2C bus 1
BMP280_ADDR = 0x76 # Address of the BMP280 sensor

# Read temperature register (example register 0xFA for BMP280)
def read_temperature():
    temp_msb = i2c_bus.read_byte_data(BMP280_ADDR, 0xFA)
    temp_lsb = i2c_bus.read_byte_data(BMP280_ADDR, 0xFB)
    temp_xlsb = i2c_bus.read_byte_data(BMP280_ADDR, 0xFC)
    raw_temp = (temp_msb << 12) | (temp_lsb << 4) | (temp_xlsb >> 4)
    temperature = raw_temp / 100.0 # Convert based on sensor datasheet
    return temperature

try:
    while True:
        temp = read_temperature()
        print(f"Temperature: {temp} C")
        time.sleep(2)
except KeyboardInterrupt:
    print("Exiting...")
#### Explanation
- Uses smbus.SMBus(1) to initialize I2C communication on bus 1.
- Reads temperature data from BMP280 registers.
- Continuously prints temperature readings every 2 seconds.

## Conclusion
This lab demonstrates:
- Interrupts using a PIR motion sensor with GPIO.
- I2C Bus Communication with a temperature sensor.
- Practical Python programming to interact with hardware components.
By completing this lab, students gain hands-on experience in embedded systems development using the Raspberry Pi.
## Questions
### Post your responses in Moodle
1. Interrupt Handling: Explain the role of the GPIO.add_event_detect() function in the interrupt-handling script. How does it help the Raspberry Pi handle GPIO inputs more efficiently compared to polling?
  The function listens for an event, which is a value passed into the function when it is instantiated. In this case, the function listens for a signal coming from the specified pin. The pin is connection to the motion detector, which sends a signal when it detects something. This helps the pi handle inputs more efficiently because, according to the OPi.GPIO Documentation, it is a threaded callback function so it runs at the same time as the rest of the program and unlike polling it is not going to miss the change in state of an input while the CPU is busy working on other things.
2. Callback Functions: Describe how the motion_detected() function in the GPIO script is triggered. What conditions must be met for this function to run?

In the add_event_detect function, the trigger value is set to GPIO.RISING, which means that its true when the state of the electrical signal of the pin being measured is changing from LOW to HIGH. This is the condition that must be met for the callback function to run.

I2C Communication: In the I2C sensor script, why do we use the smbus.SMBus(1) function? What does the number 1 signify in this context?

This function is to create an SMBus object so that we can access our device that is using the I2C protocol. The reason we use 1 is because that is the port number on our pi of the I2C device.

Data Register Access: Explain how the temperature data is read from the BMP280 sensor. What is the significance of reading multiple bytes (e.g., temp_msb, temp_lsb, and temp_xlsb)?
 Temperature is read from the sensor, which collects it’s readings as bits. Thus, we need to read multiple bytes of data and do binary operations on them in order to combine the data and convert them into a temperature in celsius.

Challenge Question:
Integrating Multiple Sensors: Using what you’ve learned from this lab, design and implement a system that combines the PIR motion sensor and the ultrasonic sensor to create a simple interactive project. You are building a proximity-based alarm system that:
- Detects motion with the PIR sensor.
- Measures distance with the ultrasonic sensor to check if an object is approaching.
Describe the wiring connections, write a high-level plan for your Python script, and explain how interrupts, analog input, and I2C communication will be utilized in your system. Be able to demonstrate your solution.