Objective: To understand and visualize data paths in a Raspberry Pi by performing basic I/O operations, observing CPU and memory interactions, and examining data flow between peripherals.

Materials Needed:
- Raspberry Pi
- Raspbian OS
- Python installed
- LED, resistor (330Ω), jumper wires, breadboard
- External USB storage device

Background: A data path refers to the flow of data between different components of a system. In a Raspberry Pi, data flows between the CPU, RAM, storage, GPIO pins, and external peripherals like USB devices. Understanding these paths is crucial for optimizing performance and troubleshooting issues.

Part 1: Understanding CPU and Memory Data Flow
1. Open a terminal on the Raspberry Pi.
2. Use the following command to monitor CPU and memory usage:
3. htop
4. Observe how different processes consume CPU and memory resources.
5. Run a Python script to perform an arithmetic operation and monitor resource usage:
6. import numpy as np
7. import time
9. data = np.random.rand(1000000)
10. start_time = time.time()
11. result = np.sum(data)
12. print(f"Computation completed in {time.time() - start_time} seconds")
13. Note how the computation affects CPU and memory load.

Part 2: GPIO Data Path Visualization
1. Connect an LED to GPIO pin 18 with a 330Ω resistor in series.
2. Run the following Python script to control the LED:
3. import RPi.GPIO as GPIO
4. import time
6. GPIO.setmode(GPIO.BCM)
7. GPIO.setup(18, GPIO.OUT)
9. for _ in range(10):
10. GPIO.output(18, GPIO.HIGH)
11. time.sleep(0.5)
12. GPIO.output(18, GPIO.LOW)
13. time.sleep(0.5)
15. GPIO.cleanup()
16. Observe how data flows from the script to the GPIO pin, controlling the LED.

Part 3: Data Flow Between Storage Devices
1. Insert a USB storage device into the Raspberry Pi.
2. Use the following command to identify the device:
3. lsblk
4. Copy a file from the Raspberry Pi to the USB device and measure the time taken:
5. time cp largefile.txt /media/pi/USB_DRIVE/
6. Observe how data is transferred between the internal storage and the external device.

Analysis and Conclusion:
- Explain how data flows through the CPU, RAM, and storage during computations.
  The python script is saved in storage. When the script is run, the instructions get loaded into memory. As the CPU begins executing the computation, it requests data from memory using memory addresses. The data is fetched from memory and calculations are made on the data in the CPU based on the instructions retrieved. Some instructions will have the CPU send data back to memory to be saved. Some instructions will send data into storage for more permanent data storage.
- Describe how GPIO interactions facilitate data movement to external devices.
- Discuss the efficiency of data transfers between different storage media.